## Slide 1: 第2部 RTコンポーネント作成入門
宮本 信彦
国立研究開発法人産業技術総合研究所
ロボットイノベーション研究センター
ロボットソフトウェアプラットフォーム研究チーム

## Slide 2: 資料(USBメモリで配布)
2
ppt
  第2部、第3部のスライド
WEBページ(手順を記載したページ)
  第2部(Windows)
  第2部(Ubuntu)
  第3部
Installer(OpenRTM-aist-1.2.1版 Windows用インストーラ)
  OpenRTM-aistのインストールに問題があった場合に使用してください
script
  この講習で使うシミュレータのインストールスクリプト(Ubuntu用)
EXE
  EV3SimulatorComp.exe(シミュレータ)
sample
  RobotController(本実習で作成するコンポーネントの見本)
Notes: 2

## Slide 3: 資料
3
USBメモリが挿せない場合は以下からダウンロード
  https://openrtm.org/openrtm/ja/tutorial/irex2019
Notes: 3

## Slide 4: インストールの確認(Windows)
4
OpenRTM-aist
  OpenRTM-aist-1.2.1-RELEASE_x86_64.msi
  インストール後に再起動する(2回再起動を必要とする環境もある)
Python
  python-3.7.5-amd64.msi
  OpenRTM-aistの64bit版をインストールする場合はPythonも64bit版をインストールする。
CMake
  cmake-3.15.4-win64-x64.msi
Doxygen
  doxygen-1.8.14-setup.exe
Visual Studio
  Visual Studio 2019
Notes: 4

## Slide 5: インストールの確認(Ubuntu)
5
OpenRTM-aist
  $ wget https://raw.githubusercontent.com/OpenRTM/OpenRTM-aist/master/scripts/pkg_install_ubuntu.sh
  $ pkg_install_ubuntu.sh -l all --yes
CMake
  $ sudo apt-get install cmake cmake-gui
Doxygen
  $ sudo apt-get install doxygen
Java
  $ sudo apt-get install openjdk-8-jdk
Code::Blocks(任意)
  $ sudo apt-get install codeblocks
EV3SimulatorComp
  sudo apt install git premake4 freeglut3-dev
  $ wget https://raw.githubusercontent.com/OpenRTM/RTM_Tutorial_EV3/master/script/install_ev3_simulator.sh
  sh install_ev3_simulator.sh
Notes: 5

## Slide 6: 実習内容
6
シミュレータ上の車輪型移動ロボット(Educator Vehicle)の操作を行うコンポーネントの作成
  GUIにより目標速度入力
  タッチセンサがオンの時に停止
Notes: 6

## Slide 7: Educator Vehicle概要
7
LEGO Mindstorms EV3の組み立て例の一つ
駆動車輪
タッチセンサ
EV3
Notes: 7

## Slide 8: 全体の手順
8
RTC Builderによるソースコード等のひな型の作成
ソースコードの編集、ビルド
  ビルドに必要な各種ファイルを生成
    CMakeLists.txtの編集
    CMakeにより各種ファイル生成
  ソースコードの編集
    RobotController.h、 RobotController.cppの編集
  ビルド
    Visual Studio、Code::Blocks
RTシステムエディタによるRTシステム作成、動作確認
  RTシステム作成
    データポート接続、コンフィギュレーションパラメータ設定
Notes: 8
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 9
コンポーネント開発ツール
RTC Builderについて

## Slide 10: RTC Builder
10
コンポーネントのプロファイル情報を入力し，ソースコード等のひな型を生成するツール
  C++、Python、Javaのソースコードを出力
Notes: 10
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 11: RTC Builderの起動
11
起動する手順
  Windows(OpenRTM-aist 1.2)
    デスクトップのショートカットをダブルクリック
  デスクトップのショートカットがない場合
    Windows 8.1
      「スタート」→「アプリビュー(右下矢印)」→「OpenRTM-aist 1.2.1」→「OpenRTP」
      ※同じフォルダに「RTSystemEditorRCP」がありますが、これはRTC Builderが使えないので今回は「OpenRTP」を起動してください。
    Windows 10
      左下の「ここに入力して検索」にOpenRTPと入力して、表示されたOpenRTPを起動
  Ubuntu
    以下のコマンドを入力
    $ openrtp
Notes: 11
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 12: RTC Builderの起動
12
Windows 8.1
デスクトップ
スタート画面
アプリビュー
Notes: 12
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 13: RTC Builderの起動
13
Windows 10
左下の「ここに入力して検索」に「OpenRTP」と入力
Notes: 13
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 14: RTC Builderの起動
14
Notes: 14
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 15: RTC Builderの起動
15
Notes: 15
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 16: プロジェクト作成
16
RobotControllerコンポーネントのスケルトンコードを作成する。
  車輪型移動ロボット操作コンポーネント
    GUIでロボットを操作
    タッチセンサがオンの場合に停止
Notes: 16
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 17: 資料
17
USBメモリで配布
  「WEBページ」フォルダのHTMLファイルを開く
    チュートリアル
      チュートリアル(EV3、Windows、第2部) _ OpenRTM-aist.html
      チュートリアル(EV3、Ubuntu、第2部) _ OpenRTM-aist.html
もしくはRTミドルウェア講習会のページからリンクをクリック
  チュートリアル(第2部、Windows)
  チュートリアル(第2部、Ubuntu)
Notes: 17
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 18: プロジェクト作成
18
OpenRTP起動時にワークスペースに指定したディレクトリに「RobotController」というフォルダが作成される
  この時点では「RTC.xml」と「.project」のみが生成されている
以下の項目が設定する
  基本プロファイル
  アクティビティ・プロファイル
  データポート・プロファイル
  サービスポート・プロファイル
  コンフィギュレーション
  ドキュメント
  言語環境
  RTC.xml
Notes: 18
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 19: 基本プロファイルの入力
19
RTコンポーネントのプロファイル情報など，コンポーネントの基本情報を設定．
コード生成，インポート/エクスポート，パッケージング処理を実行
Notes: 19
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 20: 基本プロファイルの入力
20
コンポーネント名
  RobotController
概要
  任意(Robot Controller Component)
バージョン
  任意(1.0.0)
ベンダ名
  任意
カテゴリ
  任意(Controller)
コンポーネント型
  STATIC
アクティビティ型
  PERIODIC
コンポーネントの種類
  DataFlow
最大インスタンス数
  1
実行型
  PeriodicExecutionContext
実行周期
  1000.0
概要
  任意
Notes: 20
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 21: アクティビティの設定
指定アクティビティを有効にする手順
使用するアクティビティを設定する
Notes: 21
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 22: アクティビティの設定
22
コールバック関数 | 処理
onInitialize | 初期化処理
onActivated | アクティブ化されるとき1度だけ呼ばれる
onExecute | アクティブ状態時に周期的に呼ばれる
onDeactivated | 非アクティブ化されるとき1度だけ呼ばれる
onAborting | ERROR状態に入る前に1度だけ呼ばれる
onReset | resetされる時に1度だけ呼ばれる
onError | ERROR状態のときに周期的に呼ばれる
onFinalize | 終了時に1度だけ呼ばれる
onStateUpdate | onExecuteの後毎回呼ばれる
onRateChanged | ExecutionContextのrateが変更されたとき1度だけ呼ばれる
onStartup | ExecutionContextが実行を開始するとき1度だけ呼ばれる
onShutdown | ExecutionContextが実行を停止するとき1度だけ呼ばれる
Notes: 22
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 23: アクティビティの設定
23
以下のアクティビティを有効にする
  onInitialize
  onActivated
  onDeactivated
  onExecute
Documentationは適当に書いておいてください
  空白でも大丈夫です
Notes: 23
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 24: データポートの設定
データポートを追加する手順
InPort、OutPortの追加、設定を行う
Notes: 24
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 25: データポートの設定
以下のInPortを設定する
  in
    データ型： RTC::TimedBooleanSeq
    他の項目は任意
    ※TimedBooleanと間違えないように注意してください。
以下のOutPortを設定する
  out
    データ型： RTC::TimedVelocity2D
    他の項目は任意
    ※TimedVelocity3D型、TimedVector2D型と間違えないようにしてください
Notes: 25
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 26: データポートについて
連続したデータを通信するためのポート
以下の例はデータフロー型がpush、サブスクリプション型がflush、インターフェース型がcorba_cdrの場合
Notes: 26
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 27: RTC::TimedVelocity2D型について
ExtendedDataTypes.idlで定義されている移動ロボットの速度を表現するためのデータ型
  vx: X軸方向の速度
  vy: Y軸方向の速度(車輪が横滑りしないと仮定すると0)
  va: Z軸周りの角速度
vxで直進速度、vaで回転速度を設定
Notes: 27
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 28: コンフィギュレーションの設定
コンフィギュレーションパラメータを追加する手順
コンフィギュレーションパラメータの追加、設定を行う
Notes: 28
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 29: コンフィギュレーションの設定
以下のコンフィギュレーションパラメータを設定する
  speed_x
    データ型：double
    デフォルト値： 0.0
    制約条件：-1.5<x<1.5
    Widget：slider
    Step: 0.01
    他の項目は任意
  speed_r
    データ型：double
    デフォルト値： 0.0
    制約条件：-2.0<x<2.0
    Widget：slider
    Step: 0.01
    他の項目は任意
GUI(スライダー)による移動ロボットの操作ができるようにする
Notes: 29
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 30: コンフィギュレーションパラメータの制約、Widgetの設定
制約条件：0<=x<=100
Widget：slider
Step：10
制約条件：0<=x<=100
Widget：spin
Step：10
Widget：text
RT System Editorでコンフィギュレーションパラメータを編集する際にGUIを表示する
Notes: 30
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 31: コンフィギュレーションパラメータの制約、Widgetの設定
制約条件：(0,1,2,3)
Widget：checkbox
制約条件：(0,1,2,3)
Widget：ordered_list
制約条件：(0,1,2,3)
Widget：radio
Notes: 31
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 32: EV3のタッチセンサ
前部の左右にタッチセンサを搭載
  TimedBooleanSeq型(bool型の配列)のデータ型で入力
    配列の0番目が右側、1番目が左側に対応
Notes: 32
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 33: ドキュメントの設定
各種ドキュメント情報を設定
今回は適当に設定しておいてください。
  空白でも大丈夫です
Notes: 33
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 34: 言語の設定
実装する言語，動作環境に関する情報を設定
Notes: 34
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 35: スケルトンコードの生成
基本タブからコード生成ボタンを押すことでスケルトンコードが生成される
  Workspace\RobotController以下に生成
    ソースコード
      C++ソースファイル(.cpp)
      ヘッダーファイル(.h)
        このソースコードにロボットを操作する処理を記述する
    CMakeの設定ファイル
      CMakeLists.txt
    rtc.conf、RobotController.conf
    以下略
  ファイルが生成できているかを確認してください
Notes: 35
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 36
ソースコードの編集、RTCのビルド

## Slide 37: 手順
37
ビルドに必要な各種ファイルを生成
  CMakeLists.txtの編集
  CMakeにより各種ファイル生成
ソースコードの編集
  RobotController.hの編集
  RobotController.cppの編集
ビルド
  Windows： Visual Studio
  Ubuntu： Code::Blocks
Notes: 37
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 38: CMake
38
ビルドに必要な各種ファイルを生成
  CMakeLists.txtに設定を記述
    RTC Builderでスケルトンコードを作成した時にCMakeLists.txtも生成されている
Notes: 38
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 39: ビルドに必要なファイルの生成
39
CMakeを使用する
  Windows 8.1
    「スタート」→「アプリビュー(右下矢印)」→「CMake」→「CMake (cmake-gui)」
  Windows 10
    左下の「ここに入力して検索」にCMakeと入力して表示されたCMake(cmake-gui)を起動
  Ubuntu
    コマンドで「cmake-gui」を入力
Notes: 39
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 40: cmake-guiの起動
40
Windows 8.1
デスクトップ
スタート画面
アプリビュー
Notes: 40
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 41
41
Windows 10
cmake-guiの起動
左下の「ここに入力して検索」に「cmake」と入力
Notes: 41
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 42: ビルドに必要なファイルの生成
42
CMakeLists.txtをcmake-guiにドラックアンドドロップ
  CMakeLists.txtはRTC Builderで生成したプロジェクトのフォルダ
  (例： C:\workspace\RobotController)
Notes: 42
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 43: ビルドに必要なファイルの生成
43
Notes: 43
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 44: ビルドに必要なファイルの生成
44
Notes: 44
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 45: CMake 3.14以降の場合
45
ビルド環境の設定
Visual Studio 2019 → Visual Studio 16 2019
Visual Studio 2017 → Visual Studio 15 2017
Code::Blocks → CodeBlocks – Unix Makefiles
※貸し出したPCでは「Visual Studio 14 2015」を指定
X64を選択する。
設定後、Finishボタンを押す
Notes: 45
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 46: CMake 3.13以前の場合
46
Notes: 46
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 47: ビルドに必要なファイルの生成
47
Notes: 47
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 48: ビルドに必要なファイルの生成
48
Notes: 48
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 49: ソースコードの編集
49
Notes: 49
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 50: ソースコードの編集
50
CMake-guiのバージョンが古い場合は「Open Project」ボタンがないため、ファイルをダブルクリックして開く
  Windows
    buildフォルダの「RobotController.sln」をダブルクリックして開く
  Ubuntu
    buildフォルダの「RobotController.cbp」をダブルクリックして開く
Notes: 50
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 51: ソースコードの編集
51
Windows
  Visual Studioが起動
Ubuntu
  Code::Blocksが起動
Notes: 51
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 52: ソースコードの編集
52
RobotController.hの編集
Visual Studio
Code::Blocks
Notes: 52
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 53: ソースコードの編集
53
RobotController.hの編集
Notes: 53
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 54: ソースコードの編集
54
RobotController.cppの編集
  詳細はUSBメモリの資料を参考にしてください
Visual Studio
Code::Blocks
Notes: 54
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 55: ソースコードの編集
55
RobotController.cppの編集
Notes: 55
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 56: ソースコードの編集
56
RobotController.cppの編集
Notes: 56
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 57: ソースコードの編集
57
データを読み込む手順
Notes: 57
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 58: ソースコードの編集
58
データを書き込む手順
Notes: 58
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 59: ソースコードのコンパイル
59
Visual Studio
Code::Blocks
  成功した場合、実行ファイルが生成される
    Windows
      build\srcフォルダのRelease(もしくはDebug)フォルダ内にRobotControllerComp.exeが生成される
    Ubuntu
      build/srcフォルダにRobotControllerCompが生成される
Notes: 59
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 60
システム構築支援ツール
RT System Editorについて

## Slide 61: RT System Editor
61
RTCをGUIで操作するためのツール
  データポートを接続してデータを転送できるようにする
  サービスポートの接続
  RTCをアクティブ化して処理を開始する
  非アクティブ化、リセット、終了
  コンフィギュレーションパラメータの操作
  実行コンテキストの操作
  複合化
  マネージャからRTCを起動
  作成したRTシステムの保存、復元
Notes: 61
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 62: RT System Editorの起動
62
Notes: 62
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 63: RT System Editorの画面構成
63
Notes: 63
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 64: RobotControllerコンポーネントの動作確認
64
シミュレータコンポーネントと接続してシミュレータ上のロボットを操作するRTシステムを作成する
  ネームサーバーを起動する
  EV3Simulatorコンポーネントを起動する
    Windows
      配布USBメモリのEXEフォルダ内「 EV3SimulatorComp.exe 」をダブルクリック
    Ubuntu
      配布USBメモリ内のスクリプトでインストール
        $ sh install_ev3_simulator_usb.sh
      EV3SimulatorRTC/buildに移動して以下のコマンドを実行
        $ src/EV3SimulatorComp
  RobotControllerコンポーネント起動
  EV3SimulatorコンポーネントとRobotControllerコンポーネントを接続して「All Activate」を行う
Notes: 64
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 65: ネームサーバーの起動
65
オブジェクトを名前で管理するサービス
  RTCを一意の名前で登録する
    RT System Editor等のツールはネームサーバーから名前でRTCの参照を取得する
起動する手順
Notes: 65
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 66: ネームサーバーの起動
66
OpenRTM-aist 1.1.2以前の手順
  Windows 8.1
    「スタート」→「アプリビュー(右下矢印)」→「OpenRTM-aist 1.x.x」→「Start Naming Service」
  Windows 10
    左下の「ここに入力して検索」にStart Naming Serviceと入力して起動
  Ubuntu
    $ rtm-naming
Notes: 66
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 67: RobotControllerコンポーネントの動作確認
67
シミュレータコンポーネントと接続してシミュレータ上のロボットを操作するRTシステムを作成する
  ネームサーバーを起動する
  EV3Simulatorコンポーネントを起動する
    Windows
      配布USBメモリのEXEフォルダ内「 EV3SimulatorComp.exe 」をダブルクリック
    Ubuntu
      配布USBメモリ内のスクリプトでインストール
        $sudo sh install_ev3_simulator.sh
      EV3SimulatorRTC/buildに移動して以下のコマンドを実行
        src/EV3SimulatorComp
  RobotControllerコンポーネント起動
    Windows
      build\srcフォルダのRelease(もしくはDebug)フォルダ内にRobotControllerComp.exeが生成されているためこれを起動する
    Ubuntu
      build/srcフォルダにRobotControllerCompが生成されているためこれを起動する
  RobotControllerコンポーネント、EV3Simulatorコンポーネントを接続して「All Activate」を行う
Notes: 67
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 68: データポートの接続
RTCが見えない場合は>をクリックする
Notes: 68
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 69: データポートの接続
Notes: 69
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 70: データポートの接続
Notes: 70
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 71: アクティブ化
Notes: 71
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 72: ボタンが表示されない場合
OpenRTPを一旦終了する
再度OpenRTPを起動、システムダイアグラムを表示する。
デスクトップのショートカットでOpenRTPを起動
Notes: 72
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 73: コンフィギュレーションパラメータの操作
73
コンフィギュレーションパラメータをRTシステムエディタから操作する
Notes: 73
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 74: 動作確認
74
タッチセンサがオンになった時に停止した場合
タッチセンサがオンになっても停止しない場合
Notes: 74
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 75: 失敗した場合
75
Deactivate SystemsボタンでRTCを非アクティブ化
RobotController0を右クリックしてExitを選択して終了する。
再度ビルド、実行して動作確認をする
Notes: 75
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 76: RTコンポーネントの状態遷移
RTCには以下の状態が存在する
  Created
    生成状態
    実行コンテキストを生成し、start()が呼ばれて実行コンテキストのスレッドが実行中(Runnning)状態になる
    自動的にInactive状態に遷移する
  Inactive
    非活性状態
    activate_componentメソッドを呼び出すと活性状態に遷移する
    RT System Editor上での表示は青
  Active
    活性状態
    onExecuteコールバックが実行コンテキストにより実行される
    リターンコードがRTC_OK以外の場合はエラー状態に遷移する
    RT System Editor上での表示は緑
  Error
    エラー状態
    onErrorコールバックが実行コンテキストにより実行される
    reset_componentメソッドを呼び出すと非活性状態に遷移する
    RT System Editor上での表示は赤
  終了状態
Notes: 76
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 77: RTコンポーネントの状態遷移(生成直後)
Notes: 77
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 78: RTコンポーネントの状態遷移(アクティブ化)
Notes: 78
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 79: システムの保存
Notes: 79
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 80: システムの復元
以下の内容を復元
  ポート間の接続
  コンフィギュレーション
  「Open and Create Restore」を選択した場合はマネージャからコンポーネント起動
Notes: 80
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 81: 非アクティブ化、終了
非アクティブ化
終了
Notes: 81
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 82: RTコンポーネントの状態遷移(非アクティブ化)
Notes: 82
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 83
実機との接続

## Slide 84: EV3実機との接続
EV3とノートPCを無線LANで接続
  EV3が無線LANアクセスポイントになる
注意事項
  EV3はパーツを取り外した状態で配っているのでチュートリアルに記載した手順で組み立ててください。
  ノートPCに複数のネットワークインターフェースが存在する場合にRTCの通信ができなくなる可能性があります。
    問題が発生した場合は個別に対応します。
  EV3アクセスポイント接続後はインターネットに接続できなくなります。
  EV3アクセスポイント接続後に、起動済みのネームサーバーとRTCは再起動してください。
  EV3が起動しない場合は、チュートリアルページの手順でリセットを試みてください。
Notes: 84
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 85: EV3との接続
電源投入
  中央のボタンを押す
無線LANアクセスポイントの利用
  EV3を無線LANアクセスポイント化、RTCやネームサーバーの起動を行うためには、手動でスクリプトファイルを実行する必要があります
    ボタン操作で「File Browser」→「scripts」→「start_ap.sh」を選択
Notes: 85
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 86: EV3との接続
無線LANアクセスポイントとの接続
  SSID、パスワードはEV3のシールに記載
  接続後にネームサーバーと起動済みのRTCは再起動する
  接続手順(Windows)
    画面右下のネットワークアイコンをクリック
    ev3_xxに接続後、パスワードを入力
Notes: 86
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 87: ネームサーバーとの接続
Notes: 87
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 88: 起動済みのRTC、ネームサーバー再起動
ネームサーバーを再起動する
  OpenRTM-aist 1.2の場合はネームサーバー起動ボタンで再起動
  OpenRTM-aist 1.1.2の場合はネームサーバーのプロセス終了後、「Start Naming Service」を再度実行
RTC再起動
  RTCをexitするか、RTC起動時に表示したウインドウの×ボタンを押して終了する
  実行ファイル(RobotControllerComp.exe)を再度実行
Notes: 88
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 89: ポートの接続
RobotController0とEducatorVehicle0を接続後にRTCをアクティブ化して動作確認をする
※ここでEV3Simulatorは使用しません
Notes: 89
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 90
RTC Builder
補足

## Slide 91: リセット
RTCがエラー状態に遷移した場合にエディタ上には赤く表示される。
以下の操作で非アクティブ状態に戻す
Notes: 91
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 92: RTコンポーネントの状態遷移(エラー)
Notes: 92
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 93: RTコンポーネントの状態遷移(リセット)
Notes: 93
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 94: サービスポートの設定
サービスポートの追加、インターフェースの追加、設定を行う
Notes: 94
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 95: サービスポートの設定
インターフェースを追加する
Notes: 95
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 96: サービスポートの設定
コード生成後、Pythonの場合はidlcompile.bat(idlcompile.sh)を起動する
インターフェースの設定を行う
Notes: 96
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 97: サービスポートの設定
IDLファイルについて
  プログラミング言語に非依存のインターフェース定義言語
コンシュマー側でプロバイダ側のecho、get_valueなどのオペレーションを呼び出す
Notes: 97
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 98: RTC Builderに関する設定
Notes: 98
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 99: RTC Builderに関する設定
Notes: 99
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 100: 独自のデータ型の利用
独自のデータ型でデータポートの通信を行う手順
  IDLファイルを作成する
    MyDataType.idlを任意のフォルダ(ここではC:\UserDefType)作成
    別のIDLファイルをインクルードしている場合は同じフォルダにコピーする
Notes: 100
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 101: 独自のデータ型の利用
独自のデータ型でデータポートの通信を行う手順
  RTC Builderの設定でIDLファイルの存在するディレクトリを追加
Notes: 101
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 102: 独自のデータ型の利用
独自のデータ型でデータポートの通信を行う手順
Notes: 102
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 103
RT System Editor
補足

## Slide 104: コネクタプロファイルの設定
項目 | 設定内容
Name | 接続の名称
DataType | ポート間で送受信するデータの型．ex)TimedOctet,TimedShortなど
InterfaceType | データを送信方法．ex)corba_cdrなど
DataFlowType | データの送信手順．ex)push, pullなど
SubscriptionType | データ送信タイミング．送信方法がPushの場合有効．New, Periodic, Flushから選択
Push Rate | データ送信周期(単位：Hz)．SubscriptionTypeがPeriodicの場合のみ有効
Push Policy | データ送信ポリシー．SubscriptionTypeがNew，Periodicの場合のみ有効． all，fifo，skip，newから選択
Skip Count | 送信データスキップ数．Push PolicyがSkipの場合のみ有効
Notes: 104
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 105: コネクタプロファイルの設定
InterfaceTye
  データの送信方法
  1.1.2ではcorba_cdr(CORBAによる通信)のみ選択可能
  1.2.0では以下の通信方法も選択可能になる予定
    direct(同一プロセスで起動したRTC間でデータを直接変数に渡す)
    shared_memory(共有メモリによる通信)
DataFlowType
  データの送信手順
    Push
      OutPortがInPortにデータを送る
    Pull
      InPortがOutPortに問い合わせてデータを受け取る
SubscriptionType
  データ送信タイミング(DataFlowTypeがPush型のみ有効)
    flush(同期)
      バッファを介さず即座に同期的に送信
    new(非同期)
      バッファ内に新規データが格納されたタイミングで送信
    periodic(非同期)
      一定周期で定期的にデータを送信
Push Policy(SubscriptionTypeがnew、periodicのみ有効)
  データ送信ポリシー
    all
      バッファ内のデータを一括送信
    fifo
      バッファ内のデータをFIFOで１個ずつ送信
    skip
      バッファ内のデータを間引いて送信
    new
      バッファ内のデータの最新値を送信(古い値は捨てられる)
Notes: 105
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 106: コネクタプロファイルの設定
DataFlowType
  Push
  Pull
Notes: 106
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 107: コネクタプロファイルの設定
SubscriptionType
  flush(同期)
  new、 periodic(非同期)
Notes: 107
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 108: コネクタプロファイルの設定
項目 | 設定内容
Buffer length | バッファの大きさ
Buffer full policy | データ書き込み時に，バッファフルだった場合の処理．overwrite，do_nothing，blockから選択
Buffer write timeout | データ書き込み時に，タイムアウトイベントを発生させるまでの時間(単位:秒)
Buffer empty policy | データ読み出し時に，バッファが空だった場合の処理．readback，do_nothing，blockから選択
Buffer read timeout | データ読み出し時に，タイムアウトイベントを発生させるまでの時間(単位:秒)
Notes: 108
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 109: サービスポートについて
コマンドレベルのやり取りを行うための仕組み
  任意のタイミングで操作を行いたい時などに使用
    例えばロボットアームのサーボを停止させる、ハンドを閉じる等
コンシューマ側がプロバイダ側が提供する関数群(オペレーション、メソッド)を呼び出す
インターフェースはIDLファイルで定義する。
Notes: 109
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 110: サービスポートの接続
Notes: 110
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 111: コンフィギュレーションパラメータについて
パラメータを外部から操作する仕組み
  コンポーネント作成後に変更が必要なパラメータを設定する
    例えばデバイスが接続されているCOMポート番号の設定等
Notes: 111
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 112: コンフィギュレーションパラメータの設定
Notes: 112
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 113: コンフィギュレーションパラメータの設定
方法1
方法2
Notes: 113
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 114: マネージャの操作
CameraViewerComp.exe、OpenCVCameraComp.exeのプロセスではマネージャが起動している
  マネージャがコンポーネントを起動する
Notes: 114
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 115: マネージャの操作
Notes: 115
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 116: マネージャの操作
マスターマネージャの起動、RT System Editorからの操作によるRTCの生成までの手順を説明する
  rtc.confの設定
    「manager.is_master」を「YES」に設定して起動するマネージャをマスターに設定する
      manager.is_master: YES
    モジュール探索パスの設定
      manager.modules.load_path: ., C:\\Program Files (x86)\\OpenRTM-aist\\1.1.2\\Components\\C++\\Examples\\vc12
  作成したrtc.confを設定ファイルの指定してrtcd.exeを起動する
    rtcdはコマンドプロンプトからrtcd.exeを入力するか、OpenRTM-aistをインストールしたフォルダからコピーして使用する
    rtcdはマネージャの起動のみを行う
      ～Comp.exeは起動時に特定のコンポーネントの起動も行う
    RT Syetem Editorのネームサービスビューにマネージャが表示される
Notes: 116
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 117: マネージャの操作
モジュールのロード
Notes: 117
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 118: マネージャの操作
モジュールのロード
Notes: 118
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 119: マネージャの操作
RTCの生成
Notes: 119
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 120: 実行コンテキストの操作
Notes: 120
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 121: 実行コンテキストの操作
実行周期の設定
Notes: 121
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 122: 実行コンテキストの操作
実行コンテキストの関連付け
  RTC起動時に生成した実行コンテキスト以外の実行コンテキストと関連付け
    関連付けた実行コンテキストでRTCを駆動させる
  他のRTCとの実行を同期させる
Notes: 122
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 123: 実行コンテキストの操作
実行コンテキストの関連付け
Notes: 123
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 124: 複合コンポーネントの操作
複合コンポーネントの生成
Notes: 124
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 125: 複合コンポーネントの操作
複合コンポーネントの生成
Type
  以下の3種類から選択可能
    PeriodicECShared
      実行コンテキストの共有
    PeriodicStateShared
      実行コンテキスト、状態の共有
    Grouping
      グループ化のみ
Notes: 125
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 126: 複合コンポーネントの操作
Notes: 126
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 127: 複合コンポーネントの操作
Notes: 127
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 128: ゾンビの削除
RTCのプロセスが異常終了する等してネームサーバーにゾンビが残った場合、以下の手順で削除する
Notes: 128
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 129: RT System Editorに関する設定
Notes: 129
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.